WattsLog
4/4/2020
Ultrasonic detector is using A4, A5 for I/O and those are dedicated pins on an Arduino Uno for SDA/SCL. Move the Ultrasonic detector to A2, A3 and verify that I2C using A4, A5 works correctly while the Ultrasonic detector still works.

1. Verify that SmartCar_Core20191227.ino runs the robot correctly including operation of the Ultrasonic with no changes.
   Loaded up the software, had to install Arduino_IRremote library. Not sure why that was not required before, possibly because I haven't compiled and uploaded the main program before. Verified successfully by using the IR remote to trigger progrem 2, obstacle-avoidance mode, and it was using ultrasonic detector to find obstacles, stop,change direction, detect whether it was clear ahead, and then continuing. By holding the SmartCar in my hand I could simulate the same behavior with my hand in front of the detector.
2. Modify SmartCar_Core20191227.ino for Ultrasonic detector to use A2, A3.
   Version 1.0.1, changes defines for ECHO_PIN and TRIG_PIN
   Hardware: spliced wires for the two control pins so they could reach the A2, A3 solder points on the daughter board.
3. Verify that the robot still runs correctly including operation of the Ultrasonic detectors.
   Verified in the same way as in step 1.
4. Verify that I2C works with the INA219.
5. Calibrate all four of the INA219 modules.
  1. Calibration test circuit.
  2. Code: ina219_calibrate.ino
  3. INA219_I2C_ADDRESS4 0x45 A0 = 1 A1 = 1.
     ina219Reading_mA = 1000
     extMeterReading_mA = 1020
  4. INA219_I2C_ADDRESS3 0x44 A0 = 0 A1 = 1
     ina219Reading_mA = 1000
     extMeterReading_mA = 1000
  5. INA219_I2C_ADDRESS2 0x41 A0 = 1 A1 = 0
     ina219Reading_mA = 1000
     extMeterReading_mA = 1000
  6. INA219_I2C_ADDRESS1 0x41 A0 = 0 A1 = 0
     ina219Reading_mA = 1000
     extMeterReading_mA = 1010
6. Wire up the four INA219 modules.
7. Add the getVoltageCurrentPower code integrated into the SmartCarCore