WattsLog
4/4/2020
Ultrasonic detector is using A4, A5 for I/O and those are dedicated pins on an Arduino Uno for SDA/SCL. Move the Ultrasonic detector to A2, A3 and verify that I2C using A4, A5 works correctly while the Ultrasonic detector still works.

1. Verify that SmartCar_Core20191227.ino runs the robot correctly including operation of the Ultrasonic with no changes.
   Loaded up the software, had to install Arduino_IRremote library. Not sure why that was not required before, possibly because I haven't compiled and uploaded the main program before. Verified successfully by using the IR remote to trigger progrem 2, obstacle-avoidance mode, and it was using ultrasonic detector to find obstacles, stop,change direction, detect whether it was clear ahead, and then continuing. By holding the SmartCar in my hand I could simulate the same behavior with my hand in front of the detector.
2. Modify SmartCar_Core20191227.ino for Ultrasonic detector to use A2, A3.
   Version 1.0.1, changes defines for ECHO_PIN and TRIG_PIN
   Hardware: spliced wires for the two control pins so they could reach the A2, A3 solder points on the daughter board.
3. Verify that the robot still runs correctly including operation of the Ultrasonic detectors.
   Verified in the same way as in step 1.
4. Verify that I2C works with the INA219.
5. Calibrate all four of the INA219 modules.
  1. Calibration test circuit.
  2. Code: ina219_calibrate.ino
  3. INA219_I2C_ADDRESS4 0x45 A0 = 1 A1 = 1.
     ina219Reading_mA = 1000
     extMeterReading_mA = 1020
  4. INA219_I2C_ADDRESS3 0x44 A0 = 0 A1 = 1
     ina219Reading_mA = 1000
     extMeterReading_mA = 1000
  5. INA219_I2C_ADDRESS2 0x41 A0 = 1 A1 = 0
     ina219Reading_mA = 1000
     extMeterReading_mA = 1000
  6. INA219_I2C_ADDRESS1 0x40 A0 = 0 A1 = 0
     ina219Reading_mA = 1000
     extMeterReading_mA = 1010
6. Wire up the four INA219 modules.
  1. Create schematic drawing.
  2. Create wiring diagram and connection table
  3. Prepare cable for all interconnections
  4. Drill INA219 mounting holes
  5. Pre-assemble INA219 hardware, test fit
  6. Disassemble INA219 from mounting
  7. Desolder wireless coil from power PCB
  8. Glue wireless charging coil to underside of chassis
  9. Re-solder wireless coil to power PCB
  10. Attach power PCB to top of lower chassis
  11. Drill RpiZero mounting holes
  12. Assemble RpiZero to top chassis platform
      This step resulted in tearing the AIY connector ribbon cable off the board. RpiZero still operates and the GPIO ports are now available.
  13. Install battery charging cable and wiring management
  14. Wire INA219-1 through INA219-4
  15. Wire battery, wireless charger, Uno and RpiZero
  16. Install wiring harness and wiring management
  17. Re-install INA219 modules to mountings
  18. Install final connection to I2C
7. Add the getVoltageCurrentPower code integrated into the SmartCarCore
  1. Modified getVoltageCurrentPower to get4VoltageCurrentPower
  2. Power up, smelled smoke, unplugged all, found voltage on Rpi was out of spec. Battery is putting out 7.7v when being charged and USB voltage must be from 4.75v to 5.25v. Rpi worked OK with no issues when charger was not plugged in.
  3. Program works fine without Rpi plugged in. Uno is OK with higher voltage.
  4. Battery pack automatically turns ON when charger is plugged in. I was expecting that with the battery charging I could have it ON or OFF, controlled by the switch.
  5. With charger plugged in and charging:
    1. Uno: E=7.79v I=80mA P=620mW
    1. Rpi: E=7.81v I=0mA P=0mW
    2. Motors: E=7.82 I=10mA P=60mW
    3. Chg: E=4.31v I=420mA P=1800mW
  2. With charger plugged in and NOT charging:
    1. Uno: E=7.68v I=80mA P=620mW
    2. Rpi: E=7.69v I=0mA P=0mW
    3. Motors: E=7.70 I=10mA P=60mW
    4. Chg: E=.04v I=-1mA P=0mW
  2. With charger unplugged and battery pack OFF:
    1. Uno: E=0.71v I=0mA P=0mW
    2. Rpi: E=.72v I=0mA P=0mW
    3. Motors: E=.73 I=0mA P=0mW
    4. Chg: E=.04v I=-1mA P=0mW
    5. Uno was still powered from the USB cable at 4.9v. Unplugging the USB cable (for programming) turned off the power to the Uno and it stopped. Without the USB cable from Uno to workstation the serial monitor was no longer available to report EIP data, so testing with MQTT will be required to see that it still works – no reason to think it would not.